## Slide 1
Team 10 SHEETAL.L REG:01FE21BEC401
PAVAN G.N REG:01FE21BEC402
KARTHIK M REG:01FE21BEC403
LALITA .S REG:01FE21BEC404
RTOS LAB
Review - I

## Slide 2
Problem statement
A waste management facility would like to automate of plastic present in municipal waste according to type of plastic. Help the facility by designing a suitable application.
Assumptions
Assuming only the plastic waste is directly placed at the conveyor belt of machine.
Work is to separate the 2 types of plastic using the IR sensor response and ARM 7 Controller (LPC2148).
Stepper motor used to separate the 2 type of plastic at end of conveyor belt.

## Slide 3
BLOCK DIAGRAM
ARM Controller
(LPC2148)
IR Sensor
Stepper Motor B
position
Power 3.3v
Stepper
Motor A conveyor
5v DC
5v DC
Motor
Driver
Motor
Driver

## Slide 4
Flow chart
START
IR Value
Motor B at
Position 1
Motor B at Position 2
Value
Conveyor
motor
<= 0x310
> 0x310

## Slide 5
Working :
When system is ON the Conveyer motor is used to run the conveyor belt until the plastic waste reaches the sensor position .
IR sensor used to sense or to read the different analogous readings from reflection of the IR light .
The analog readings are converted to digital form using internal ADC of ARM controller-LPC2148.
IR basically gives the solution to separate the 2 types of plastic like transparent and fully coloured plastic.
Depending upon the digital values, position of stepper Motor B is adjusted in between 1 and 2. Position shifting can be achieved by rotating it 180 degree.
After the decision on the separation of the plastic, conveyor motor is made to run until the waste is dumped to appropriate section of separation box.
Above process is repeated for each plastic piece.

## Slide 6
Pin configuration :
Stepper motor A: (For conveyor belt)
- Pin number from P1.16 to P1.19
Stepper motor B: (Rotates container)
- Pin number from P0.8 and P0.11
ADC (Analog to Digital convertor):
- Pin number from P0.25(channel - AD0.4)

## Slide 7
Thank you